## Slide 1: Electron Paramagnetic Resonance and Dynamic Nuclear Polarisation CH916
Gavin W Morley,
Department of Physics,
University of Warwick

## Slide 2
Overview
Electron paramagnetic resonance
  What it is
  Why it’s useful
Dynamic nuclear polarization
  Why it’s useful
  What it is

## Slide 3
Overview
Electron paramagnetic resonance
  What it is
  Why it’s useful
Dynamic nuclear polarization
  Why it’s useful
  What it is

## Slide 4
Overview
Electron paramagnetic resonance
  What it is
  …NMR for electrons

## Slide 5
Electron paramagnetic resonance (EPR)
… or electron spin resonance (ESR)
… or electron magnetic resonance (EMR)
… or ferromagnetic resonance (FMR)

## Slide 6
Magnetism
Electron spins tend to:
Paramagnetism: follow
Diamagnetism: oppose
Ferromagnetism: ignore
…an applied magnetic field

## Slide 7
From Steven Brown’s NMR lecture:

## Slide 8
Magnetic resonance
Isidor Isaac Rabi (1898 – 1988)
Energy of a spin ½
Photon energy
Magnetic field
An isolated spin I = ½ has m = ±½
m = +½
m = -½

## Slide 9
Magnetic resonance
Isidor Isaac Rabi (1898 – 1988)
Energy of a spin ½
Photon energy
Magnetic field
m = +½
m = -½

## Slide 10
Magnetic resonance
Isidor Isaac Rabi (1898 – 1988)
Energy of a spin ½
Magnetic field
Photon energy
Magnetic field
Photons reflected
m = +½
m = -½

## Slide 11
Magnetic resonance
Isidor Isaac Rabi (1898 – 1988)
Energy of a spin ½
Magnetic field
Photon energy
Magnetic field
Photons reflected
m = +½
m = -½

## Slide 12
Magnetic resonance
Isidor Isaac Rabi (1898 – 1988)
Energy of a spin ½
Magnetic field
Photon energy
Magnetic field
Photons reflected
m = +½
m = -½

## Slide 13
Magnetic resonance
Energy of a spin S = ½
Magnetic field, Bz
Magnetic field, Bz
Photons reflected
Energy gap |ΔE| = g μB Bz
g is the EPR equivalent of chemical shielding in NMR,
µB is the Bohr magneton
Pieter Zeeman (1865 - 1943)
Notes: Zeeman effect

## Slide 14
Magnetic resonance condition
Energy of a spin S = ½
Magnetic field, Bz
Magnetic field, Bz
Photons reflected
Energy gap |ΔE| = g μB Bz = hfres
= ħωres
Notes: Zeeman effect

## Slide 15
Magnetic field, Bz
Photons reflected
Electron paramagnetic resonance
J van Tol, L-C Brunel & RJ Wylde, Rev Sci Instrum 76, 076101 (2005)
Bruker
fres = 10 GHz
fres = 240 GHz

## Slide 16
Electron paramagnetic resonance
Energy of a spin system
Magnetic field, Bz
Magnetic field, Bz
Photons reflected
S = ½
ms = ±½
I = ½
mI = ±½ (= m)
Energy gap |ΔE| = g μB Bz
Notes: mu_N is the nuclear magneton and it is ~1000 times smaller than mu_B

## Slide 17
Electron paramagnetic resonance
Energy of a spin system
Magnetic field, Bz
Magnetic field, Bz
Photons reflected
Energy gap |ΔE| = g μB Bz
S = ½
ms = ±½
I = ½
mI = ±½ (= m)

## Slide 18
Energy of a spin system
Magnetic field, Bz
Photons reflected
A
mI = ½ mI = -½
Magnetic field, Bz
Electron paramagnetic resonance
S = ½
ms = ±½
I = ½
mI = ±½ (= m)
Energy gap |ΔE| = g μB Bz ± A/2

## Slide 19
Photons reflected
A
Magnetic field, Bz
TEMPO
£20/g from Aldrich
J van Tol, L-C Brunel & RJ Wylde, Rev Sci Instrum 76, 076101 (2005)
Electron paramagnetic resonance
Stable free radicals:
BDPA
Nitroxides
DPPH
mI = ½ mI = -½

## Slide 20
Photons absorbed
A
Magnetic field, Bz
TEMPO
£20/g from Aldrich
J van Tol, L-C Brunel & RJ Wylde, Rev Sci Instrum 76, 076101 (2005)
Electron paramagnetic resonance
mI = ½ mI = -½

## Slide 21
Photons absorbed
A
Magnetic field, Bz
TEMPO
£20/g from Aldrich
J van Tol, L-C Brunel & RJ Wylde, Rev Sci Instrum 76, 076101 (2005)
Electron paramagnetic resonance
mI = 1 mI = 0 mI = -1

## Slide 22
Magnetic field, B
Electron paramagnetic resonance
Magnetic field modulation
(~10 to 100 kHz)
Advantage: noise only at
modulation frequency
Photons absorbed
Differential
absorption
mI = 1 mI = 0 mI = -1

## Slide 23
Differentialabsorption
Magnetic field, B
TEMPO
£20/g from Aldrich
J van Tol, L-C Brunel & RJ Wylde, Rev Sci Instrum 76, 076101 (2005)
Electron paramagnetic resonance
A
mI = 1 mI = 0 mI = -1

## Slide 24
Differentialabsorption
Magnetic field, B
TEMPO
£20/g from Aldrich
J van Tol, L-C Brunel & RJ Wylde, Rev Sci Instrum 76, 076101 (2005)
Electron paramagnetic resonance
mI = 1 mI = 0 mI = -1

## Slide 25
Electron paramagnetic resonance
spectrometer
Console
Computer
Electromagnet (up to 1.5 T) or superconducting magnet for higher field
S
Microwave bridge

## Slide 26
Electron paramagnetic resonance
spectrometer
S
Bridge
source
detector
Microwave resonator
Modulation coils

## Slide 27
Electron paramagnetic resonance
spectrometer
S
Bridge
source
detector
Microwave resonator
Modulation coils

## Slide 28
Electron paramagnetic resonance
spectrometer
S
Bridge
source
detector
Microwave resonator
Modulation coils

## Slide 29
Electron paramagnetic resonance
spectrometer
CW EPR so far…
Pulsed EPR next

## Slide 30
Pulsed electron paramagnetic resonance spectrometer
S
Bridge
High power pulsed source
Protected detector
Microwave resonator
Modulation coils off

## Slide 31
Pulsed electron paramagnetic resonance

## Slide 32
Pulsed electron paramagnetic resonance
Bres
resonance condition g mB Bres = h f
f
p/2
Free induction decay (FID) on timescale T2*
Polarize (thermalise) on timescale T1

## Slide 33
Pulsed EPR
f
p/2
J van Tol, L-C Brunel & RJ Wylde, Rev Sci Instrum 76, 076101 (2005)
~100 MHz width
Pulse width < 500 MHz
Resonator ringing  deadtime
Short T2 and T2* compared to NMR
Homogeneous (T2) can be much longer than inhomogeneous (T2*) so most pulsed EPR uses spin echo

## Slide 34
Rotating frame

## Slide 35
Rotating frame

## Slide 36
Spin echo
In rotating frame

## Slide 37
Spin echo
In rotating frame

## Slide 38
Spin echo decay
Erwin L Hahn (born 1921) Photo: AIP Emilio Segre Visual Archives, Stephen Jacobs Collection

## Slide 39
Spin echo decay
Erwin L Hahn (born 1921) Photo: AIP Emilio Segre Visual Archives, Stephen Jacobs Collection
Notes: Hahn echo

## Slide 40
Pulsed EPR
Double electron-electron resonance (DEER) allows distances between two electron spins in the range 2 to 6 nm to be measured (cf < 1 nm by NMR for two nuclear spins)
Dipolar coupling α 1/r3
Site directed spin labelling with
one or more TEMPO

## Slide 41
Energy of a spin system
Magnetic field, Bz
Photons reflected
A
Magnetic field, Bz
Electron nuclear double resonance (ENDOR)
mI = ½ mI = -½
S = ½
ms = ±½
I = ½
mI = ±½ (= m)
Energy gap |ΔE| = g μB Bz ± A/2

## Slide 42
Electron nuclear double resonance (ENDOR)
Why do ENDOR instead of NMR?
only need ~1010 spins instead of ~1015
NMR may be difficult near the electron spin
Energy of a spin system
Magnetic field, Bz
Energy gap |ΔE| = g μB Bz ± A/2

## Slide 43
Electron nuclear double resonance (ENDOR)
B0 is static magnetic field
B1 is EPR magnetic field
B2 is NMR magnetic field
Energy of a spin system
Magnetic field, B0
Energy gap |ΔE| = g μB B0 ± A/2

## Slide 44
ENDOR for quantum computing
Classical Quantum
computer computer
Bits Qubits
0 or 1 α 0 + β 1
Notes: A normal computer stores information as bits that can be 1 or 0. A quantum computer uses qubits: two level quantum systems such as spins 1/2

## Slide 45
Spin qubits in silicon
Image by
Manuel Vögtli (UCL)
Notes: Phosphorus atoms in silicon are called donors because they donate an electron to the silicon at RT. This is used in modern computers. I work at helium temperatures where the atoms bind their electrons. The donor nucleus has a nuclear spin and the bound electron has a spin also. This is an envelope wavefunction

## Slide 46
Other EPR applications
  Quality control in beer, wine etc
  Radiation dose received by teeth

## Slide 47
Overview
Electron paramagnetic resonance
  What it is
  Why it’s useful
Dynamic nuclear polarization
  Why it’s useful
  What it is

## Slide 48
Dynamic nuclear polarization (DNP)
Dynamic nuclear polarization
  More signal

## Slide 49
Dynamic nuclear polarization (DNP)
Define polarization as:
n2
n1
ΔE
Thermal (Boltzmann) equilibrium:

## Slide 50
Dynamic nuclear polarization (DNP)
Boltzmann polarization:
So transfer electronic
polarization to nuclei

## Slide 51
Electron paramagnetic resonance
Energy of a spin system
Magnetic field, Bz
Magnetic field, Bz
Photons reflected
Energy gap |ΔE| = g μB Bz
S = ½
ms = ±½
I = ½
mI = ±½ (= m)
Notes: Show these energy levels again

## Slide 52
Energy of a spin system
Magnetic field, Bz
Photons reflected
A
mI = ½ mI = -½
Magnetic field, Bz
Electron paramagnetic resonance
S = ½
ms = ±½
I = ½
mI = ±½ (= m)
Energy gap |ΔE| = g μB Bz ± A/2
Notes: …including the hyperfine term, and then redraw the energy levels at some fixed magnetic field

## Slide 53
Dynamic nuclear polarization (DNP)
Initial polarizations:
Electrons > 95%
Nuclei < 0.1%
For 8.6 T and 3 K
Notes: At 8.6T and 3K, electronic polarization is 95% and nuclear polarization is 0.06%.

## Slide 54
Dynamic nuclear polarization (DNP)
Nuclear magnetic resonance (NMR)

## Slide 55
Dynamic nuclear polarization (DNP)
Electron paramagnetic resonance (EPR)

## Slide 56
Dynamic nuclear polarization (DNP)
Forbidden transition
 Overhauser Effect
Electron paramagnetic resonance (EPR)

## Slide 57
Magnetic resonance
Energy of a spin system
Magnetic field, Bz
Magnetic field, Bz
Photons reflected
Energy gap |ΔE| = g μB Bz
S = ½
ms = ±½
I = ½
mI = ±½ (= m)

## Slide 58
Breit-Rabi diagram
Energy of a spin system
Magnetic field, Bz
Magnetic field, Bz
Photons reflected
A
Gregory Breit (1899-1981)
mI = ½ mI = -½
Energy gap |ΔE| ≈ g μB Bz ± A/2
...in high enough magnetic fields
Notes: Breit-Rabi diagram

## Slide 59
Breit-Rabi diagram
Energy of a spin system
Magnetic field, Bz
Triplet, F = 1: ↑↑
(↑↓ + ↓↑)/√2
↓↓
Singlet, F = 0: (↑↓ - ↓↑)/√2
For a coupled two-spin system at low magnetic field, the spin states of the two spins are not good quantum numbers. Instead:
Energy gap |ΔE| = A
...at zero magnetic field
A

## Slide 60
Dynamic nuclear polarization (DNP)
more Forbidden
at high magnetic fields
Electron paramagnetic resonance (EPR)

## Slide 61
Dynamic nuclear polarization (DNP)
also gets weaker at high magnetic fields
Solid effect DNP

## Slide 62
Dynamic nuclear polarization (DNP)
also gets weaker at high magnetic fields
Solid effect DNP

## Slide 63
Dynamic nuclear polarization (DNP)
also get weaker at high magnetic fields
Cross effect Thermal Mixing
e-
e-
n
e-
e-
n
e-
e-
n
n

## Slide 64
Dynamic nuclear polarization (DNP)
Ray Dupree, Steven Brown, Mark Newton, Kevin Pike, Andrew Howes, Tom Kemp, Mark Smith at Warwick,
see KJ Pike et al, J Mag Res 215, 1 (2012), also Griffin Group (MIT)

## Slide 65
Dynamic nuclear polarization (DNP)
Ray Dupree, Steven Brown, Mark Newton, Kevin Pike, Andrew Howes, Tom Kemp, Mark Smith at Warwick,
see KJ Pike et al, J Mag Res 215, 1 (2012)

## Slide 66
Dynamic nuclear polarization (DNP)
ENDOR-DNP:
A S Brill, PRA 66 043405 (2003)
EPR + NMR = Electron nuclear double resonance (ENDOR)

## Slide 67
Dynamic nuclear polarization (DNP)
ENDOR-DNP:
A S Brill, PRA 66 043405 (2003)
EPR + NMR = Electron nuclear double resonance (ENDOR)

## Slide 68
Dynamic nuclear polarization (DNP)
ENDOR-DNP:
A S Brill, PRA 66 043405 (2003)
EPR + NMR = Electron nuclear double resonance (ENDOR)

## Slide 69
Dynamic nuclear polarization
240 GHz excitation, A/ħ = 16 MHz
Background Our research
A
Notes: Need resolved HFS. Intrinsic linewidth less than 0.3microTesla: 80kHz! Hyperfine A=16MHz

## Slide 70
Background Our research
Dynamic nuclear polarization
240 GHz excitation, A/ħ = 16 MHz
ENDOR-DNP at 4 K
Notes: High field resonance is 8% of total after DNP, 33% before. 15N@C60 gives 62% polarization with enhancement of 1000. Intrinsic linewidth less than 0.3microTesla: 80kHz! Hyperfine A=16MHz

## Slide 71
Dynamic nuclear polarization
Temperature jump
plus
gain x50 from DNP
and x200 from temp
x10,000 total
See Ardenkjaer-Larsen et al, PNAS 100, 10158 (2003)

## Slide 72
Dynamic nuclear polarization
Temperature jump with dissolution
plus
Arnaud Comment and Rolf Gruetter, Lausanne

## Slide 73
Conclusion
Electron paramagnetic resonance
  What it is
  Why it’s useful
Dynamic nuclear polarization
  Why it’s useful
  What it is